## Slide 1
Christoph Hamsen
Berlin Crypto Meetup
Quantum Cryptography
from basics of quantum mechanics to secure key distribution
May contain traces of atom and quantum optics!

## Slide 2: Who am I?
Studied Physics @ TU Ilmenau, MIT, TU Munich and Harvard
Researched on quantum optics for PhD @ MPQ
Developed software for robots @ Magazino
Bringing IT security to software @ SSE
Podcasts enthusiast (Logbuch Netzpolitik, Lage der Nation) and frequent visitor to c3!
The speaker is not a cryptographer!

## Slide 3: Cryptography and Key Distribution
Alice
Bob
Communication should be secure!
Authentic
Confidential
Integrity
Choose Transport Layer Security (TLS)!
v1.2 or higher!
Select Cipher suite
DHE – RSA – AES128 – SHA256
Key Exchange
Authentication
Encryption
Message Authentication
DHE – RSA – AES128 – SHA256
How to securely exchange the key?
Only computationally secure
Eve
Quantum Key Distribution offers physical security

## Slide 4: Enter the photon!
< 1900: Light is a wave!
> 1900: Light consists of particles (photons)
> 1980: First single-photon sources
  Photon cannot be split!
  Measurements are irreversible.
100%
0%
50%
Transmission:
Probability:
Image sources: Anton Paar (wiki.anton-paar.com), oPhysics.com, Wikipedia
Polarization
Polarizer
Image sources:
David Nadlinger @ Ion Trap Quantum Computing Group at University of Oxford
Rempe Group @ Max Planck Institute of Quantum Optics

## Slide 5: Quantum Key Distribution
Alice
Bob
“0”
“1”
h/v basis
“0”
“1”
diag. basis
RNG
RNG
RNG
1
1
0
1
0/1
0/1
1
0/1
0
0
0
0
1
0/1
1
1
0
0/1
1
1
0
0
1
0/1
Protocol:
Alice sends random values in random bases
Bob measures in random bases
Alice communicates chosen bases via classical channel
Both compare random subset of values
Eve
1
0/1
0/1
0/1
0/1
0/1
0/1
1
0/1
0/1
0
0/1
25% error rate on comparison
á la “BB84”
Provably secure!
“No-cloning theorem”
Vadim Makarov – Quantum Hacker
Source: http://www.vad1.com/

## Slide 6: Attacks & Vulnerabilities
Intercept and Resend
Denial of Service
Photon Number Splitting
Trojan Horse
  Detection Probability
Alice
Bob
= 1.5
= 0.2
Poisson distribution
_____________________________________________________
N. Jain, B. Stiller, I. Khan, V. Makarov, C. Marquardt and G. Leuchs,
"Risk Analysis of Trojan-Horse Attacks on Practical Quantum Key Distribution Systems“,
IEEE 21 (3), 168-177 (2015)
single-photon sources
privacy amplification
other protocols, e.g. decoy state QKD
Original source unclear

## Slide 7: Hardware/Implementation attacks
Attack | Target component | Tested system
Intersymbol interference | intensity modulator in Alice | research system
K. Yoshino et al., poster at QCrypt (2016) |  | 
Laser damage | any | ID Quantique, research system
V. Makarov et al., Phys. Rev. A 94, 030302 (2016) |  | 
Spatial efficiency mismatch | receiver optics | research system
M. Rau et al., IEEE J. Quantum Electron. 21, 6600905 (2015); S. Sajeed et al., Phys. Rev. A 91, 062301 (2015) |  | 
Pulse energy calibration | classical watchdog detector | ID Quantique
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015) |  | 
Trojan-horse | phase modulator in Alice | SeQureNet
I. Khan et al., presentation at QCrypt (2014) |  | 
Trojan-horse | phase modulator in Bob | ID Quantique
N. Jain et al., New J. Phys. 16, 123030 (2014); S. Sajeed et al., arXiv:1704.07749 |  | 
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, Proc. SPIE 88990N (2013) |  | 
Shot-noise calibration | classical sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research system
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research system
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research system
I. Gerhardt et al., Nat. Commun. 2, 349 (2011); L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 
need hardening of components and implementation!
Table by V.Makarov: http://www.vad1.com/

## Slide 8: Real world QKD
Handle losses due to e.g. sources, quantum channel, detector, Eve, ...
Key Distillation
Alice
Bob
Quantum channel
Trans. photons
Public channel
Raw key
Basis reconciliation
Subset comparison
Error correction
Privacy amplification
Key!
Key!
Transmission losses ultimately limit QKD distance!

## Slide 9: “Applications”
Many research groups world-wide
  Components
  Theory
Commercial systems
  IDQuantique, MagiQ Technologies, QuintessenceLabs, SeQureNet, …
Several long-distance test networks…

## Slide 10
17 km (fiber length)
14 km
4 km
www.swissquantum.com
ID Quantique Cerberis system (2010)
QKD to another node
(14 km)
QKD to another node
(4 km)
Key manager
WDMs
Classical encryptors:
L2, 2 Gbit/s
L2, 10 Gbit/s
L3 VPN, 100 Mbit/s
Slide taken from V.Makarov (http://www.vad1.com/)

## Slide 11
Q. Zhang, talk at QCrypt 2014
Slide taken from V.Makarov (http://www.vad1.com/)

## Slide 12
Global quantum key distribution
Slide adapted from V.Makarov (http://www.vad1.com/)

## Slide 13
Chinese quantum satellite (launched 2016)
Bell test over 1200 km
Satellite-to-ground QKD at 1 kbit/s
Quantum teleportation over 1400 km
J. Yin et al., Science 356, 1140 (2017)
S.-K. Liao et al., arXiv:1707.00542
J.-G. Ren et al., arXiv:1707.00934
Slide taken from V.Makarov (http://www.vad1.com/)

## Slide 14: Challenges & Developments
Challenges
  Requires classical crypto, e.g. for authentication
  Faint effects hard to implement
  e2e encryption (mobiles?)
  Standardization
Developments
  Quantum Relays and Repeaters
  Device-independent QKD (E91 protocol)
  Multi-mode, quantum signatures, quantum one-way functions, …
Alice
Bob
RNG
RNG
RNG

## Slide 15: the end
Alice
Bob
Bye
Thank you for your attention!
Eve
You’re welcome ;-)
https://www.linkedin.com/in/hamsen/